## Slide 1: EcoStruxure Power Design- Ecodial
Presented by: Rashmi Kumari
Schneider Electric
How to manually select the conductor size in Ecodial
Notes: Chapter | Slide nbr | Title/objectives | Timing
Training introduction – presentation and objectives |  |  | 17min
Introduction | 2 | Round table | 15’
 | 3 | Training program – Objectives | 2’
Why change management? |  |  | 8min
Why change management? | 5 | Context of change management for ecorealXL trainings | 2’
 | 6 | Psychological reactions to change | 6’
Driving change management |  |  | 42min
Driving change management | 8-12 | Communication adapted to each phase | 31’
 | 12-14 | Obtaining the users’ support | 11’
Managing trainings |  |  | 25min
Managing trainings | 17 | Managing time and rhythm | 15’
 | 18 | Managing attention | 10’
15min break |  |  | 
Preparing trainings |  |  | 30min
Preparing trainings | 21 | Discussion – How to prepare ecorealXL trainings? | 15’
 | 22 | Prerequisites for the trainer | 2’
 | 23-26 | Checking and preparing the material | 8’
 | 27 | Informing trainees | 2’
 | 28 | Enrolling trainees | 3’
Feedbacks on training |  |  | 21min
Feedbacks on training | 30 | Discussion – What should you do after each training? | 15’
 | 31 | Checking and cleaning | 3’
 | 32 | Send feedbacks | 3’
Conclusion |  |  | 20min
Conclusion | 34 | Checking expectations – remaining questions | 20’

## Slide 2
How to manually select the conductor size in Ecodial
Create a network
Provide cable parameters in properties tab by selecting cable in network area.
Calculate the network
Application will size cable conductor automatically based on sizing current and the cable installation method input which has was provided in the “ properties tab”

## Slide 3
How to manually select the conductor size in Ecodial
Application has sized the cable
Ph- 6x300AL
PEN-6X300AL
Here maximum permissible CSA mm2 is selected as -300 sqmm
So, application has sized cable with 300 CSA with 6 runs .

## Slide 4
How to manually select the conductor size in Ecodial
How to size cable conductors manually with different number of run and cross section for individual loads?
Lets consider ,If you want to select 400Sq. Mm cable for feeder.
Select particular load /feeder from network area
Select properties area
Click on ‘ maximum permissible CSA sq mm”
Cable CSA ,starting from 90sqm - 630sq mm will appear in drop down box
Select 400Sq.mm csble.
Calculate the project
Ecodial will size the cable based on the maximum permissible CSA which you have selected as 400sq. Mm and application will accordingly adjust the cable run based on sizing current .

## Slide 5
How to manually select the conductor size in Ecodial
Notes: .

## Slide 6
How to manually select the conductor size in Ecodial- Final Result
– Final result
Notes: .