How to modify the BIOS in order to access the MEBX menu by ‘CTRl+P’ keys

It depends of the BIOS version but it could happen that the simple access to MEBX Menu by the ‘Ctrl+P’ key combination doesn’t work.
In that case, please follow the following steps to modify the BIOS:
After that you should succeed to enter the MEBX menu using ‘Ctrl+P’
- You should create a bootable USB key with un-zipped files extract from ‘S782V112.zip’ attached in this FAQ.
- Then plug the USB Key on the Rack and follow the steps:
Step	Subject	Description
1	Disable ME	Turn off AC power and move JME jumper to 2-3 pin.
2	Enter DOS	boot into DOS.
3	BIOS Flash Command	Flash the BIOS with command (see last screenshot): afudos filename.bin /p /b /n /x /me /r
4	Turn off AC	After BIOS flash complete, turn AC power off.
5	Resume ME	Move JME back to 1-2 pin
6	Clear CMOS	Move JCMOS to 2-3 pin for 5 seconds to clear CMOS then move back to 1-2 pin.
7	Enter BIOS	Power on system and press ESC to go to BIOS setup menu.
8	Restore Default	Restore Default Setting then Save and Exit

Note that:
JME jumper
Step 1 - the JME Jumper is:

Step 6 - the JCMOS jumper is:

JCMOS jumper

The command to type in Step 3 is: