## Slide 1: Centralized security Database

## Slide 2: Centralized Security Database
Database path located inside the registry:
  HKEY_LOCAL_MACHINE\SOFTWARE\Schneider Electric\Security Editor\ProductVersion0\SERVERS\ServerPath (32bit OS)
  or
  HKEY_LOCAL_MACHINE\SOFTWARE\Wow6432Node\Schneider Electric\Security Editor\ProductVersion0\SERVERS\ServerPath (64bit OS)
  Possibility to provide an UNC Path pointing on the network (like \\ComputerName\Folder\...)
  Interesting if we have only one Writter (Server PC) and multi readers (other PCs).
On the server PC
  Share the folder containing the Security Databases
    Grant Read only access rights to all users.
     users won’t be able to modify the security profiles (Security Editor won’t start)

## Slide 3: Centralized Security Database
On every Client PC,
  change the ServerPath using the network path to access to the server PC (don’t forget the ‘\’ at the end)