## Slide 1: Offer Preview
Control Activity & Industry Services
September 2013
Momentum for Unity
M1
M1E
M1EGD

## Slide 2
Offer Feature Introduction
Performance & Migration
References
Objectives
Key topics
Programming Language Support
Communications Ports & Networks
Migrating existing Momentum Applications
Data Sheet Comparison - New vs. Existing

## Slide 3: Momentum for Unity – Available with Unity 8..0 Arriving Q4 2013
3 Top Hat CPUs - form factor fits on any existing Momentum IO Base
Performance is equivalent or better than existing Momentum
Converted applications will maintain the same free memory ratio or more
Supports LL984 or IEC, or Both
12 Mb/s mini USB for easy setup, configuration, programming and fast firmware update
Cost competitive with existing Momentum
Supported in all Unity version sizes S, M, X, XL
Share Processor DNA with PlantStruxure – New Generation CPU

## Slide 4: Processor Offer Features
Real Time Clock embedded in all Unity Momentum references
Indefinite State RAM retention in all Unity Momentum references
IO Bus Distributed IO built into all references
Converts Modsoft, Proworx, Concept to Unity
All references support MSTR/MBP_MSTR, X/XMIT
M1 supports dual serial
M1E supports Ethernet IO Scanner
M1EGD supports IO Scanner and Ethernet Global Data
Embedded Web diagnostics
Support Modbus Plus with Proxy

## Slide 5: Overview of Processor Offers
System on a Chip CPU with memory retention of State RAM and Real Time Clock
  New processor family that will power Automation platforms into the future at Schneider
  Performance equal to, or better than, existing Momentum. Even with LL984
  Momentum Option Adapter not supported
Performance to match or exceed the current, optimized Momentum processor
Ports and Services for smooth migration

## Slide 6: Processor Hardware
Mounts natively on any Momentum IO Base
Migrate to Unity without re-wiring
Enhanced LED panel for CPU, IO, Ethernet and Serial Status
Uses existing Momentum IO Label
Mini USB
@12 Mb/s
M1 has 2 Serial RJ45
M1E has 1 Ethernet & 1 Serial
IO Bus DB9
Common Architecture
Spear CPU @ 333 MHz
12 Mb/s mini USB
Embedded Real Time Clock
Memory Retention without Battery
IO Bus Distributed IO for 32 Slaves
M1E
M1
Enhanced LED’s
Wider CPU at 144mm (5.6in)
Same dimensions as PNN or JNN Option Adapter
On Board
Real Time Clock
Retention of State RAM

## Slide 7: Unity Processor References
  Unity M1 170CBU78090 – USB, IO Bus, 1 - 232/485 Serial, 1 - 485 Serial
  Unity M1E 170CBU98090 – USB, IO Bus, 1 - 232/485 Serial, 1 - Ethernet
  Unity M1E 170CBU98091 – M1E as above with Ethernet Global Data Service
USB port for easy initial configuration, programming and firmware updates
Both IEC and LL984 projects can be directly imported to Unity from Concept or Proworx
Performance is as good or better than Momentum today
Maintains the same relative free space for logic and State RAM
Pricing is competitive with Momentum today
Maintains your existing I/O and peripherals
Remove Power and disconnect peripheral & IO Bus Cables
Install Unity ‘Top Hat’ CPU onto IO Base and reconnect cables.
Some cables may need to be adapted for connector style
Import your application into Unity v8.0, build and Run
Some configuration and logic adjustments must be performed
1, 2, 3 Unity Migration
JNN or PNN Option Adapter is not supported with Unity CPU

## Slide 8: M1 Modernization
IO Bus Slave
Non-Networked
Unity Momentum M1
IO Bus Slave
1, Stand Alone CPU & IO Base
Remove Option Adapter
3. Stand Alone CPU with up to 64 IO Bus Slaves (M1 may have JNN)
2, Standalone CPU with JNN Option Adapter for clock, battery and RS485
Replace existing M1 Top Hat CPU with Unity M1 Top Hat
IO Bus Slave
IO Bus Slave
Connect up to 32 IO Bus Slaves and serial devices
(JNN no longer required)
Migration to Unity
OR
23% of all Momentum non-networked
63% have IO Bus Slaves connected
Option Adapter not supported with most functions embedded in the CPU

## Slide 9: M1E Modernization
IO Bus Slave
Ethernet Networked
Unity Momentum M1E
IO Bus Slave
1, Ethernet Networked M1E & IO Base
3. Ethernet Networked M1E with up to 64 IO Bus Slaves (M1E may have JNN)
2, Ethernet Networked M1E with JNN Option Adapter for clock, battery and RS485
Replace existing M1E Top Hat CPU with Unity M1E Top Hat
IO Bus Slave
IO Bus Slave
Connect to IO Bus Slaves with existing cable
(JNN no longer required)
Migration to Unity
OR
77% of all Momentum is networked
41% of those are networked on Ethernet
Remove Option Adapter
Option Adapter not supported with most functions embedded in the CPU

## Slide 10: Momentum & Modbus Plus
Customers that wish to remain on Modbus Plus have a Unity Momentum solution
  Using the M1E 171CBU98090 or M1EGD 171CBU98091, the Modbus Plus Proxy TCSEGDB23F24FA can be used to fully support:
    Modbus Plus Peer Cop
    Modbus Plus Global Data
    5 byte Modbus Plus message routing
    Unity programming from Modbus Plus to Unity M1E
    Single or dual cable Modbus Plus connectivity

## Slide 11: Catalog Data Sheets
Unity Momentum M1
Unity Momentum M1E
  2 M1E References
    Global Data reference added

## Slide 12: Thank You!