## Slide 1: Connecting Power Advisor Customer Sites
Automate connecting customer sites to Schneider Electric EcoStruxure™ Technology Platform to save time, drive efficiency and deliver more value
Technical Release | April 2024

## Slide 2
Why Use Cloud Connectivity?
ESP for Power Management leverages Power Advisor to delivers expert recommendations to the customer, thanks to the analysis of PME Data.
Time-consuming / requires to synchronize with the PME end-user
Tight coordination between different SE stakeholders to create the reports
Last version of PME data extractor required
Generates big ZIP files and is usually limited to 30 or 60 days of data history
Challenges with manual data extraction
(performed on-site or remotely):
Extraction is automated
PME data is continuously sent to the Power Advisor platform
Analysis can be run at any time and on any selected time ranges
Customer is ready to be upgraded to Asset Advisor ED through the PME gateway
New cloud connector is 4x faster to commission
Advantages of Cloud Connectivity
CALL TO ACTION  Cloud connectivity shall be the default mode of data acquisition
 PME data can be extracted manually (running the PME data extractor) or automatically (enabling cloud connectivity).
* Pre-requisites for ETP connector: - PME version  9.0 - Cumulative Updates 2 (CU2) - Cloud connection accepted by client - Full commercial PME license
 PA Cybersecurity Overview
Power Advisor
platform
Electrical Health
Data Quality
Alarm Health
Manual extraction of PME data
Expert
analysis
Top recommendations
Customer PME
ETP *
DS Data Hub
Cloud connectivity enabled

## Slide 3: How to Connect
How to easily connect customer sites to EcoStruxure Technology Platform to ensure data availability

## Slide 4
Edge Control Version Compatibility | PME Data Connector | PA Manual Data Extractor | PA Data Quality & Electrical Health | PA Alarm Health | PA System Health
ION-E 6 |  | ● | ● |  | 
SPM 7.x |  | ● | ● |  | 
PME 8.x |  | ● | ● |  | ● 8.2
PME 9.x PME2020 / 2021 | ●* | ● | ● | ●* | ●
PSE / PSO / PO + Advanced Reports module | ●* | ● | ● | ●* | ● (does not require Advanced Reports module)
PSO 2020 | Not supported | ● R2 | ● R2 | ● | ●
PO 2021 | Not supported | ● | ● | ● | ●
Feature Compatibility Matrix
Connection requires PME on network with accessible port for data connection
New capability
No limitation on how many assets under management (AUM) can be analyzed!
*(PME 9 CU2>)

## Slide 5
What is the process
Prerequisite: Customer has an existing service contract including PA, and PA VM has been provisioned.
New or existing customer
Log into Customer PA site
PA Administrator
PA Services Engineer
SE Ecostruxure Technology platform
Generate
Monthly data files
Accessible to PA
Browse available files and Upload selected file
Collect basic data
Collect PA-specific data
One-time process
“Would you like to upload your data automatically?”
Register and
Enable Connected Services in PME
Link PME site to PA site
(through Site Key and Contract ID)
E-mail request to link PME site
Screencap Registration
Capture Site Key
e-mail to PA Engineer
>= 30 days
5 Minutes

## Slide 6
Activating Services : Step 1 ) Registration
Settings – Registration Information
Take Screen capture
for e-mail

## Slide 7
Activating Services : Step 2 ) Enable Connected Services
Settings - Diagnostics and Services
Capture Site Key
for e-mail

## Slide 8
After Activating Services on PME:
A) Compose e-mail to request the linkage of PME to PA in the cloud.
Subject Line: PME Link to PA request for <Power Advisor Customer Name>
Content:
  Screencap of Registration screen
  Site Key from the Diagnostic Services screen.
  Contract ID ( If known).
B) Send e-mail.
  If the customer has done the PME activation, then this e-mail should be sent to the PA Service Engineer. The PA Service Engineer will then forward the information to the Power Advisor Global Administrator (serviceplan.administrator@schneider-electric.com)
  If the PA Service Engineer has done the PME activation, then this e-mail should be sent directly to the Power Advisor Administrator (serviceplan.administrator@schneider-electric.com)
Activating Services : Step 3 ) Send Link Request e-mail

## Slide 9
Notes: Closing slide